# VHDL code (all files)
## 1) vga_timing.vhd

library ieee;
use ieee.std_logic_1164.all;
use ieee.numeric_std.all;

entity vga_timing is
  port (
    clk : in std_logic;
    rst : in std_logic;

    hsync : out std_logic;
    vsync : out std_logic;
    de : out std_logic;

    x : out unsigned(9 downto 0);
    y : out unsigned(9 downto 0)
  );
end entity;

architecture rtl of vga_timing is
  constant H_VISIBLE : integer := 640;
  constant H_FRONT : integer := 16;
  constant H_SYNC : integer := 96;
  constant H_BACK : integer := 48;
  constant H_TOTAL : integer := 800;

  constant V_VISIBLE : integer := 480;
  constant V_FRONT : integer := 10;
  constant V_SYNC : integer := 2;
  constant V_BACK : integer := 33;
  constant V_TOTAL : integer := 525;

  signal hc : integer range 0 to H_TOTAL-1 := 0;
  signal vc : integer range 0 to V_TOTAL-1 := 0;
begin
  process(clk)
  begin
    if rising_edge(clk) then
      if rst='1' then
        hc <= 0;
        vc <= 0;
      else
        if hc = H_TOTAL-1 then
        hc <= 0;
        if vc = V_TOTAL-1 then
        vc <= 0;
        else
        vc <= vc + 1;
        end if;
        else
        hc <= hc + 1;
        end if;
      end if;
    end if;
  end process;

  de <= '1' when (hc < H_VISIBLE and vc < V_VISIBLE) else '0';

  x <= to_unsigned(hc, x'length) when (hc < H_VISIBLE) else (others=>'0');
  y <= to_unsigned(vc, y'length) when (vc < V_VISIBLE) else (others=>'0');

  hsync <= '0' when (hc >= H_VISIBLE + H_FRONT and hc < H_VISIBLE + H_FRONT + H_SYNC) else '1';
  vsync <= '0' when (vc >= V_VISIBLE + V_FRONT and vc < V_VISIBLE + V_FRONT + V_SYNC) else '1';
end architecture;

2) video_gen_rgb.vhd (ONLY R/G/B background)

library ieee;
use ieee.std_logic_1164.all;
use ieee.numeric_std.all;

entity video_gen_rgb is
  port (
    clk : in std_logic;
    de : in std_logic;
    x : in unsigned(9 downto 0);
    rgb : out std_logic_vector(11 downto 0)
  );
end entity;

architecture rtl of video_gen_rgb is
  signal r,g,b : unsigned(3 downto 0);
  signal xi : integer range 0 to 1023;
begin
  xi <= to_integer(x);

  process(clk)
  begin
    if rising_edge(clk) then
      if de='1' then
        if xi < 213 then
        r <= x"F"; g <= x"0"; b <= x"0"; -- Red
        elsif xi < 426 then
        r <= x"0"; g <= x"F"; b <= x"0"; -- Green
        else
        r <= x"0"; g <= x"0"; b <= x"F"; -- Blue
        end if;
      else
        r <= (others=>'0'); g <= (others=>'0'); b <= (others=>'0');
      end if;

      rgb <= std_logic_vector(r & g & b);
    end if;
  end process;
end architecture;

3) uptime_timer.vhd (HH:MM:SS uptime, reset by btnC)

library ieee;
use ieee.std_logic_1164.all;
use ieee.numeric_std.all;

entity uptime_timer is
  port (
    clk100MHz : in std_logic;
    rst : in std_logic;

    hh_tens : out unsigned(3 downto 0);
    hh_ones : out unsigned(3 downto 0);
    mm_tens : out unsigned(3 downto 0);
    mm_ones : out unsigned(3 downto 0);
    ss_tens : out unsigned(3 downto 0);
    ss_ones : out unsigned(3 downto 0)
  );
end entity;

architecture rtl of uptime_timer is
  constant ONE_SEC : unsigned(26 downto 0) := to_unsigned(100_000_000 - 1, 27);
  signal sec_cnt : unsigned(26 downto 0) := (others=>'0');
  signal tick_1hz : std_logic := '0';

  signal s1,s0,m1,m0,h1,h0 : unsigned(3 downto 0) := (others=>'0');

  procedure bcd_inc_00_59(
    signal tens : inout unsigned(3 downto 0);
    signal ones : inout unsigned(3 downto 0);
    variable carry : out std_logic
  ) is
  begin
    carry := '0';
    if ones = 9 then
      ones <= (others=>'0');
      if tens = 5 then
        tens <= (others=>'0');
        carry := '1';
      else
        tens <= tens + 1;
      end if;
    else
      ones <= ones + 1;
    end if;
  end procedure;

  procedure bcd_inc_00_99(
    signal tens : inout unsigned(3 downto 0);
    signal ones : inout unsigned(3 downto 0)
  ) is
  begin
    if ones = 9 then
      ones <= (others=>'0');
      if tens = 9 then
        tens <= (others=>'0');
      else
        tens <= tens + 1;
      end if;
    else
      ones <= ones + 1;
    end if;
  end procedure;

begin
  process(clk100MHz)
  begin
    if rising_edge(clk100MHz) then
      if rst='1' then
        sec_cnt <= (others=>'0');
        tick_1hz <= '0';
      else
        if sec_cnt = ONE_SEC then
        sec_cnt <= (others=>'0');
        tick_1hz <= '1';
        else
        sec_cnt <= sec_cnt + 1;
        tick_1hz <= '0';
        end if;
      end if;
    end if;
  end process;

  process(clk100MHz)
    variable carry_s : std_logic;
    variable carry_m : std_logic;
  begin
    if rising_edge(clk100MHz) then
      if rst='1' then
        s1 <= (others=>'0'); s0 <= (others=>'0');
        m1 <= (others=>'0'); m0 <= (others=>'0');
        h1 <= (others=>'0'); h0 <= (others=>'0');
      else
        if tick_1hz='1' then
        bcd_inc_00_59(s1, s0, carry_s);
        if carry_s='1' then
        bcd_inc_00_59(m1, m0, carry_m);
        if carry_m='1' then
        bcd_inc_00_99(h1, h0); -- uptime hours 00..99
        end if;
        end if;
        end if;
      end if;
    end if;
  end process;

  hh_tens <= h1; hh_ones <= h0;
  mm_tens <= m1; mm_ones <= m0;
  ss_tens <= s1; ss_ones <= s0;
end architecture;

4) symbology_reticle.vhd ✅ (UPDATED small reticle)

library ieee;
use ieee.std_logic_1164.all;
use ieee.numeric_std.all;

entity symbology_reticle is
  port (
    clk : in std_logic;
    de : in std_logic;
    x : in unsigned(9 downto 0);
    y : in unsigned(9 downto 0);

    hh_tens : in unsigned(3 downto 0);
    hh_ones : in unsigned(3 downto 0);
    mm_tens : in unsigned(3 downto 0);
    mm_ones : in unsigned(3 downto 0);
    ss_tens : in unsigned(3 downto 0);
    ss_ones : in unsigned(3 downto 0);

    sym_on : out std_logic;
    sym_rgb : out std_logic_vector(11 downto 0)
  );
end entity;

architecture rtl of symbology_reticle is
  constant CX : integer := 320;
  constant CY : integer := 240;

  constant YELLOW : std_logic_vector(11 downto 0) := x"FF0";
  constant WHITE : std_logic_vector(11 downto 0) := x"FFF";

  -- Small reticle parameters (shooter-like)
  constant RET_R : integer := 10;
  constant RET_THICK : integer := 1;
  constant LINE_HALF : integer := 12;

  constant R2_IN : integer := (RET_R - RET_THICK) * (RET_R - RET_THICK);
  constant R2_OUT : integer := (RET_R + RET_THICK) * (RET_R + RET_THICK);

  constant TXT1_X0 : integer := 20;
  constant TXT1_Y0 : integer := 20;
  constant TXT2_X0 : integer := 20;
  constant TXT2_Y0 : integer := 40;

  constant DATE_STR : string := "TUE 03-03-2026";

  signal xi, yi : integer range 0 to 1023;

  signal on_ring : std_logic;
  signal on_cross : std_logic;
  signal on_text1 : std_logic := '0';
  signal on_text2 : std_logic := '0';

  -- Build the uptime string in a signal so the renderer can use it
  signal UPTIME_STR : string(1 to 15) := "UPTIME 00:00:00";

  function bcd_to_char(d : unsigned(3 downto 0)) return character is
  begin
    case to_integer(d) is
      when 0 => return '0';
      when 1 => return '1';
      when 2 => return '2';
      when 3 => return '3';
      when 4 => return '4';
      when 5 => return '5';
      when 6 => return '6';
      when 7 => return '7';
      when 8 => return '8';
      when others => return '9';
    end case;
  end function;

  -- 8x8 glyphs (minimal set used by our strings)
  function glyph(c : character; row : integer) return std_logic_vector is
    variable g : std_logic_vector(7 downto 0) := (others=>'0');
  begin
    case c is
      -- digits 0..9 (same as before; include only if you want shorter file you can keep all)
      when '0' => case row is
        when 0 => g:=x"3C"; when 1 => g:=x"66"; when 2 => g:=x"6E"; when 3 => g:=x"76";
        when 4 => g:=x"66"; when 5 => g:=x"66"; when 6 => g:=x"3C"; when others => g:=x"00"; end case;
      when '1' => case row is
        when 0 => g:=x"18"; when 1 => g:=x"38"; when 2 => g:=x"18"; when 3 => g:=x"18";
        when 4 => g:=x"18"; when 5 => g:=x"18"; when 6 => g:=x"3C"; when others => g:=x"00"; end case;
      when '2' => case row is
        when 0 => g:=x"3C"; when 1 => g:=x"66"; when 2 => g:=x"06"; when 3 => g:=x"1C";
        when 4 => g:=x"30"; when 5 => g:=x"60"; when 6 => g:=x"7E"; when others => g:=x"00"; end case;
      when '3' => case row is
        when 0 => g:=x"3C"; when 1 => g:=x"66"; when 2 => g:=x"06"; when 3 => g:=x"1C";
        when 4 => g:=x"06"; when 5 => g:=x"66"; when 6 => g:=x"3C"; when others => g:=x"00"; end case;
      when '4' => case row is
        when 0 => g:=x"0C"; when 1 => g:=x"1C"; when 2 => g:=x"3C"; when 3 => g:=x"6C";
        when 4 => g:=x"7E"; when 5 => g:=x"0C"; when 6 => g:=x"0C"; when others => g:=x"00"; end case;
      when '5' => case row is
        when 0 => g:=x"7E"; when 1 => g:=x"60"; when 2 => g:=x"7C"; when 3 => g:=x"06";
        when 4 => g:=x"06"; when 5 => g:=x"66"; when 6 => g:=x"3C"; when others => g:=x"00"; end case;
      when '6' => case row is
        when 0 => g:=x"1C"; when 1 => g:=x"30"; when 2 => g:=x"60"; when 3 => g:=x"7C";
        when 4 => g:=x"66"; when 5 => g:=x"66"; when 6 => g:=x"3C"; when others => g:=x"00"; end case;
      when '7' => case row is
        when 0 => g:=x"7E"; when 1 => g:=x"66"; when 2 => g:=x"06"; when 3 => g:=x"0C";
        when 4 => g:=x"18"; when 5 => g:=x"18"; when 6 => g:=x"18"; when others => g:=x"00"; end case;
      when '8' => case row is
        when 0 => g:=x"3C"; when 1 => g:=x"66"; when 2 => g:=x"66"; when 3 => g:=x"3C";
        when 4 => g:=x"66"; when 5 => g:=x"66"; when 6 => g:=x"3C"; when others => g:=x"00"; end case;
      when '9' => case row is
        when 0 => g:=x"3C"; when 1 => g:=x"66"; when 2 => g:=x"66"; when 3 => g:=x"3E";
        when 4 => g:=x"06"; when 5 => g:=x"0C"; when 6 => g:=x"38"; when others => g:=x"00"; end case;

      -- letters used: U P T I M E and day letters T U E and maybe spaces
      when 'U' => case row is
        when 0 => g:=x"66"; when 1 => g:=x"66"; when 2 => g:=x"66"; when 3 => g:=x"66";
        when 4 => g:=x"66"; when 5 => g:=x"66"; when 6 => g:=x"3C"; when others => g:=x"00"; end case;
      when 'P' => case row is
        when 0 => g:=x"7C"; when 1 => g:=x"66"; when 2 => g:=x"66"; when 3 => g:=x"7C";
        when 4 => g:=x"60"; when 5 => g:=x"60"; when 6 => g:=x"60"; when others => g:=x"00"; end case;
      when 'T' => case row is
        when 0 => g:=x"7E"; when 1 => g:=x"5A"; when 2 => g:=x"18"; when 3 => g:=x"18";
        when 4 => g:=x"18"; when 5 => g:=x"18"; when 6 => g:=x"3C"; when others => g:=x"00"; end case;
      when 'I' => case row is
        when 0 => g:=x"3C"; when 1 => g:=x"18"; when 2 => g:=x"18"; when 3 => g:=x"18";
        when 4 => g:=x"18"; when 5 => g:=x"18"; when 6 => g:=x"3C"; when others => g:=x"00"; end case;
      when 'M' => case row is
        when 0 => g:=x"63"; when 1 => g:=x"77"; when 2 => g:=x"7F"; when 3 => g:=x"6B";
        when 4 => g:=x"63"; when 5 => g:=x"63"; when 6 => g:=x"63"; when others => g:=x"00"; end case;
      when 'E' => case row is
        when 0 => g:=x"7E"; when 1 => g:=x"60"; when 2 => g:=x"60"; when 3 => g:=x"7C";
        when 4 => g:=x"60"; when 5 => g:=x"60"; when 6 => g:=x"7E"; when others => g:=x"00"; end case;

      -- punctuation
      when ':' => case row is
        when 1 => g:=x"18"; when 2 => g:=x"18"; when 4 => g:=x"18"; when 5 => g:=x"18"; when others => g:=x"00";
      end case;
      when '-' => case row is
        when 3 => g:=x"7E"; when others => g:=x"00";
      end case;
      when ' ' => g := x"00";
      when others => g := x"00";
    end case;

    return g;
  end function;

begin
  xi <= to_integer(x);
  yi <= to_integer(y);

  -- Build UPTIME_STR safely in a clocked process (no illegal function reads)
  process(clk)
  begin
    if rising_edge(clk) then
      UPTIME_STR <= "UPTIME " &
        bcd_to_char(hh_tens) & bcd_to_char(hh_ones) & ':' &
        bcd_to_char(mm_tens) & bcd_to_char(mm_ones) & ':' &
        bcd_to_char(ss_tens) & bcd_to_char(ss_ones);
    end if;
  end process;

  -- reticle ring
  on_ring <= '1' when (de='1' and
        ((xi-CX)*(xi-CX) + (yi-CY)*(yi-CY) >= R2_IN) and
        ((xi-CX)*(xi-CX) + (yi-CY)*(yi-CY) <= R2_OUT)
        ) else '0';

  -- short crosshair arms
  on_cross <= '1' when (de='1' and (
        (yi = CY and (xi >= CX-LINE_HALF and xi <= CX+LINE_HALF)) or
        (xi = CX and (yi >= CY-LINE_HALF and yi <= CY+LINE_HALF))
        )) else '0';

  -- Text rendering (UPTIME_STR and DATE_STR)
  process(clk)
    variable relx, rely : integer;
    variable chpos, col, row : integer;
    variable c : character;
    variable g : std_logic_vector(7 downto 0);
  begin
    if rising_edge(clk) then
      on_text1 <= '0';
      on_text2 <= '0';

      if de='1' then
        -- Line 1: uptime
        relx := xi - TXT1_X0;
        rely := yi - TXT1_Y0;
        if relx >= 0 and rely >= 0 then
        chpos := relx / 8;
        col := relx mod 8;
        row := rely mod 8;

        if (rely/8 = 0) and (chpos >= 0) and (chpos < UPTIME_STR'length) then
        c := UPTIME_STR(chpos+1);
        g := glyph(c, row);
        if g(7-col)='1' then
        on_text1 <= '1';
        end if;
        end if;
        end if;

        -- Line 2: date string (fixed)
        relx := xi - TXT2_X0;
        rely := yi - TXT2_Y0;
        if relx >= 0 and rely >= 0 then
        chpos := relx / 8;
        col := relx mod 8;
        row := rely mod 8;

        if (rely/8 = 0) and (chpos >= 0) and (chpos < DATE_STR'length) then
        c := DATE_STR(chpos+1);
        g := glyph(c, row);
        if g(7-col)='1' then
        on_text2 <= '1';
        end if;
        end if;
        end if;
      end if;
    end if;
  end process;

  -- Priority: text (white) over reticle (yellow)
  process(clk)
  begin
    if rising_edge(clk) then
      if (on_text1='1' or on_text2='1') then
        sym_on <= '1';
        sym_rgb <= WHITE;
      elsif (on_ring='1' or on_cross='1') then
        sym_on <= '1';
        sym_rgb <= YELLOW;
      else
        sym_on <= '0';
        sym_rgb <= (others=>'0');
      end if;
    end if;
  end process;

end architecture;
5) overlay_engine.vhd

library ieee;
use ieee.std_logic_1164.all;

entity overlay_engine is
  port (
    clk : in std_logic;
    de : in std_logic;
    rgb_in : in std_logic_vector(11 downto 0);
    sym_on : in std_logic;
    sym_rgb : in std_logic_vector(11 downto 0);
    rgb_out : out std_logic_vector(11 downto 0)
  );
end entity;

architecture rtl of overlay_engine is
begin
  process(clk)
  begin
    if rising_edge(clk) then
      if de='1' then
        if sym_on='1' then
        rgb_out <= sym_rgb;
        else
        rgb_out <= rgb_in;
        end if;
      else
        rgb_out <= (others => '0');
      end if;
    end if;
  end process;
end architecture;

6) top_vga_overlay2.vhd

library ieee;
use ieee.std_logic_1164.all;
use ieee.numeric_std.all;

entity top_vga_overlay2 is
  port (
    clk100MHz : in std_logic;
    btnC : in std_logic;

    vgaRed : out std_logic_vector(3 downto 0);
    vgaGreen : out std_logic_vector(3 downto 0);
    vgaBlue : out std_logic_vector(3 downto 0);
    Hsync : out std_logic;
    Vsync : out std_logic
  );
end entity;

architecture rtl of top_vga_overlay2 is
  signal rst : std_logic;

  signal pix_clk : std_logic := '0';
  signal div_cnt : unsigned(1 downto 0) := (others => '0');

  signal de : std_logic;
  signal x,y : unsigned(9 downto 0);

  signal rgb_bg : std_logic_vector(11 downto 0);
  signal sym_on : std_logic;
  signal sym_rgb : std_logic_vector(11 downto 0);
  signal rgb_out : std_logic_vector(11 downto 0);

  signal hh_t, hh_o, mm_t, mm_o, ss_t, ss_o : unsigned(3 downto 0);
begin
  rst <= btnC;

  -- 100MHz -> 25MHz
  process(clk100MHz)
  begin
    if rising_edge(clk100MHz) then
      if rst='1' then
        div_cnt <= (others=>'0');
        pix_clk <= '0';
      else
        div_cnt <= div_cnt + 1;
        pix_clk <= div_cnt(1);
      end if;
    end if;
  end process;

  U_TIM: entity work.vga_timing
    port map (
      clk => pix_clk,
      rst => rst,
      hsync => Hsync,
      vsync => Vsync,
      de => de,
      x => x,
      y => y
    );

  U_BG: entity work.video_gen_rgb
    port map (
      clk => pix_clk,
      de => de,
      x => x,
      rgb => rgb_bg
    );

  U_UP: entity work.uptime_timer
    port map (
      clk100MHz => clk100MHz,
      rst => rst,
      hh_tens => hh_t,
      hh_ones => hh_o,
      mm_tens => mm_t,
      mm_ones => mm_o,
      ss_tens => ss_t,
      ss_ones => ss_o
    );

  U_SYM: entity work.symbology_reticle
    port map (
      clk => pix_clk,
      de => de,
      x => x,
      y => y,

      hh_tens => hh_t,
      hh_ones => hh_o,
      mm_tens => mm_t,
      mm_ones => mm_o,
      ss_tens => ss_t,
      ss_ones => ss_o,

      sym_on => sym_on,
      sym_rgb => sym_rgb
    );

  U_OVL: entity work.overlay_engine
    port map (
      clk => pix_clk,
      de => de,
      rgb_in => rgb_bg,
      sym_on => sym_on,
      sym_rgb => sym_rgb,
      rgb_out => rgb_out
    );

  vgaRed <= rgb_out(11 downto 8);
  vgaGreen <= rgb_out(7 downto 4);
  vgaBlue <= rgb_out(3 downto 0);
end architecture;

XDC FILE-

## =========================================================
## Basys 3 (Rev B) - VGA Overlay Project (Updated)
## Top ports:
## clk100MHz, btnC
## vgaRed[3:0], vgaGreen[3:0], vgaBlue[3:0]
## Hsync, Vsync
## =========================================================

set_property PACKAGE_PIN W5 [get_ports clk100MHz]
set_property IOSTANDARD LVCMOS33 [get_ports clk100MHz]
create_clock -add -name sys_clk_pin -period 10.00 -waveform {0 5} [get_ports clk100MHz]

set_property PACKAGE_PIN U18 [get_ports btnC]
set_property IOSTANDARD LVCMOS33 [get_ports btnC]

set_property PACKAGE_PIN G19 [get_ports {vgaRed[0]}]
set_property IOSTANDARD LVCMOS33 [get_ports {vgaRed[0]}]
set_property PACKAGE_PIN H19 [get_ports {vgaRed[1]}]
set_property IOSTANDARD LVCMOS33 [get_ports {vgaRed[1]}]
set_property PACKAGE_PIN J19 [get_ports {vgaRed[2]}]
set_property IOSTANDARD LVCMOS33 [get_ports {vgaRed[2]}]
set_property PACKAGE_PIN N19 [get_ports {vgaRed[3]}]
set_property IOSTANDARD LVCMOS33 [get_ports {vgaRed[3]}]

set_property PACKAGE_PIN J17 [get_ports {vgaGreen[0]}]
set_property IOSTANDARD LVCMOS33 [get_ports {vgaGreen[0]}]
set_property PACKAGE_PIN H17 [get_ports {vgaGreen[1]}]
set_property IOSTANDARD LVCMOS33 [get_ports {vgaGreen[1]}]
set_property PACKAGE_PIN G17 [get_ports {vgaGreen[2]}]
set_property IOSTANDARD LVCMOS33 [get_ports {vgaGreen[2]}]
set_property PACKAGE_PIN D17 [get_ports {vgaGreen[3]}]
set_property IOSTANDARD LVCMOS33 [get_ports {vgaGreen[3]}]

set_property PACKAGE_PIN N18 [get_ports {vgaBlue[0]}]
set_property IOSTANDARD LVCMOS33 [get_ports {vgaBlue[0]}]
set_property PACKAGE_PIN L18 [get_ports {vgaBlue[1]}]
set_property IOSTANDARD LVCMOS33 [get_ports {vgaBlue[1]}]
set_property PACKAGE_PIN K18 [get_ports {vgaBlue[2]}]
set_property IOSTANDARD LVCMOS33 [get_ports {vgaBlue[2]}]
set_property PACKAGE_PIN J18 [get_ports {vgaBlue[3]}]
set_property IOSTANDARD LVCMOS33 [get_ports {vgaBlue[3]}]

set_property PACKAGE_PIN P19 [get_ports Hsync]
set_property IOSTANDARD LVCMOS33 [get_ports Hsync]
set_property PACKAGE_PIN R19 [get_ports Vsync]
set_property IOSTANDARD LVCMOS33 [get_ports Vsync]